Version in ODF 1.2
## 19.211 draw:sharpness
The draw:sharpness attribute specifies the radius of the ellipse on which inner polygon corners are located. The value is a percentage, where 0% means that all corners are located on a single ellipse, while 100% means that the inner corners are located at the center point of the polygon. If r is the radius of the polygon, and s is the sharpness, the inner corners are located on a ellipse whose radius is r(100-s)/100.
Note: This attribute is only meaningful only with a draw:concave attribute with the value true.

Proposal draft
## 19.211 draw:sharpness
The draw:sharpness attribute is only evaluated for a <draw:regular-polygon> element that has the attribute draw:concave="true". In that case the outline of the drawing object is based on a basic model where points in the amout given in attribute draw:corners are evenly distrubted on a circle with center point M. Let now P and Q be two neighboured points on the circle and R the middle point of the shorter of the two arcs PQ. A straigt line is thought through center point M and point R. Now find the point T on this line with widevec MT = widevec MR cdot ( 1-s% ) , where s"%" is the value of the draw:sharpness attribute. The points P and T and the points T and Q are connected by straight sections then. Thus the drawing object has twice as many corners in all as specified in the attribute "draw:corners".
The basic model is scaled—thereby the circle might become an ellipse, so that the bounding box of the polygon has the width and height as specified in the svg:width and svg:height attributes of the <draw:regular-polygon> element.
The value of the draw:sharpness attribute is a percent value. The special case 0% means, that all corners of the drawing object are located on one ellipse; the polygon is actually convex. The special case 100% means, that all points, that are constructed as described above for point T, coincide with the center point M. The value of the draw:sharpness attribute may be negative and it may be larger than 100%.
Note: Because of intercept theorems the equation widevec {MT} = widevec {MR} cdot left(1-s"%" right) is valid for the scaled outline too.