SCA Bindings Issue 2 Proposal v3:

1) Every request message that invokes the forward interface MAY contain the wsa:From SOAP header block. The wsa:From header block, if present, specifies the Callback EPR. If wsa:From header block is not present, then the [reply endpoint] message addressing property specifies the Callback EPR. If the Callback EPR's [address] value is "http://www.w3.org/2005/08/addressing/anonymous" or " http://www.w3.org/2005/08/addressing/none" then the SCA runtime MUST generate the Invalid Addressing Header fault as specified in WS-Addressing 1.0 SOAP Binding, Section 6.4.1 [ref]. Such a fault MAY include additional [Subsubcode] wsa:OnlyNonAnonymousAddressSupported.

2) Every request message that invokes the forward interface MAY contain the wsa:MessageID SOAP header block. 

3) When the service wants to invoke the callback interface, it uses the Callback EPR from a request message, as specified in step 1, that invoked the forward interface. Once the Callback EPR is selected, the SCA runtime MUST follow the rules defined in WS-Addressing 1.0  Core Section 3.3 to invoke operations on the callback interface. In addition, when the service invokes the callback interface using a Callback EPR obtained from a message that includes a wsa:MessageID SOAP header block, the SCA runtime MUST include a wsa:RelatesTo SOAP header block in the callback request message. The wsa:RelatesTo SOAP header block MUST have the relationship type value of "http://docs.oasis-open.org/opencsa/sca-bindings/ws/callback/200812" and the related message id MUST be the wsa:MessageID of the message from which the Callback EPR was obtained.

Scenarios:

S: service with a bidirectional interface
R: reference connected to service S

The wire binding (in both directions) uses SOAP.

The forward interface consists of only one one-way operation: YouRIt()
The callback interface consists of only one one-way operation: NoYouRIt()

R invokes YouRIt(). Let's call this invocation R1 and it sets the callback address to RC1. S then calls NoYouRIt() twice: S1 and S2
R invokes YouRIt() again. Let's call this invocation R2 and it sets the callback address to RC1. S then calls NoYouRIt() once: S3
R invokes YouRIt(). Let's call this invocation R3 and it sets the callback address to RC2. S then calls NoYouRIt() twice: S4 and S5.

Wire messages: 
R1:

<soap:Envelope ...>
 <soap:Header>
   <wsa:From>
     <wsa:Address>http://example.com/callback</wsa:Address>
     <wsa:ReferenceProperties>
       <myNS:SomeID>1</myNS:SomeID>
     </wsa:ReferenceProperties>
   </wsa:From>
   <wsa:MessageID>urn:uuid:f81d4fae-7dec-11d0-a765-00a0c91e6bf6</wsa:messageID>
    ...
 </soap:Header>
 <soap:Body>
   ...
 </soap:Body>
</soap:Envelope>

S1, S2:

<soap:Envelope ...>
 <soap:Header>
   <wsa:To>http://example.com/callback</wsa:To>
   <myNS:SomeID>1</myNS:SomeID>
   <wsa:RelatesTo RelationshipType="http://docs.oasis-open.org/opencsa/sca-bindings/callback">
   urn:uuid:f81d4fae-7dec-11d0-a765-00a0c91e6bf6
   </wsa:RelatesTo>
    ...
 </soap:Header>
 <soap:Body>
   ...
 </soap:Body>
</soap:Envelope>

R2:

<soap:Envelope ...>
 <soap:Header>
   <wsa:From>
     <wsa:Address>http://example.com/callback</wsa:Address>
     <wsa:ReferenceProperties>
       <myNS:SomeID>1</myNS:SomeID>
     </wsa:ReferenceProperties>
   </wsa:From>
   <wsa:MessageID>urn:uuid:f81d4fae-8dec-11d0-a765-00a0c91e6bf6</wsa:messageID>
    ...
 </soap:Header>
 <soap:Body>
   ...
 </soap:Body>
</soap:Envelope>

S3:

<soap:Envelope ...>
 <soap:Header>
   <wsa:To>http://example.com/callback</wsa:To>
   <myNS:SomeID>1</myNS:SomeID>
   <wsa:RelatesTo RelationshipType="http://docs.oasis-open.org/opencsa/sca-bindings/callback">
   urn:uuid:f81d4fae-8dec-11d0-a765-00a0c91e6bf6
   </wsa:RelatesTo>
    ...
 </soap:Header>
 <soap:Body>
   ...
 </soap:Body>
</soap:Envelope>

R3:

<soap:Envelope ...>
 <soap:Header>
   <wsa:From>
     <wsa:Address>http://example.com/callback-other</wsa:Address>
     <wsa:ReferenceProperties>
       <myNS:SomeID>2</myNS:SomeID>
     </wsa:ReferenceProperties>
   </wsa:From>
   <wsa:MessageID>urn:uuid:f81d4fae-9dec-11d0-a765-00a0c91e6bf6</wsa:messageID>
    ...
 </soap:Header>
 <soap:Body>
   ...
 </soap:Body>
</soap:Envelope>

S4, S5:

<soap:Envelope ...>
 <soap:Header>
   <wsa:To>http://example.com/callback-other</wsa:To>
   <myNS:SomeID>2</myNS:SomeID>
   <wsa:RelatesTo RelationshipType="http://docs.oasis-open.org/opencsa/sca-bindings/callback">
   urn:uuid:f81d4fae-9dec-11d0-a765-00a0c91e6bf6
   </wsa:RelatesTo>
    ...
 </soap:Header>
 <soap:Body>
   ...
 </soap:Body>
</soap:Envelope>