UDDI Spec TC

Technical Note

UDDI as the registry for ebXML components

Document identifier:

uddi-spec-tc-tn-uddi-ebxml

Location:

http://www.oasis-open.org/committees/uddi-spec/doc/tn/uddi-spec-tc-tn-uddi-ebxml-20030131.doc

Author:

Keisuke Kibakura, FUJITSU

Editors:

Luc Clément, Microsoft

Daniel Feygin, Unitspace

Contributors:

Joel Munter, Intel

Claus von Riegen, SAP

Max Voskob, MSI Business Solutions

Abstract:

This document describes the way to model ebXML-based services and ebXML components such as CPP and BPSS, and provides a practical guidance on how to use a UDDI V2 registry as the registry for ebXML.

Status:

This document is a working draft. This is updated periodically on no particular schedule.

Committee members should send comments on this technical note to the uddi-spec@lists.oasis-open.org list. Others should subscribe to and send comments to the uddi-spec-comment@lists.oasis-open.org list. To subscribe, send an email message to uddi-spec-comment-request@lists.oasis-open.org with the word "subscribe" as the body of the message.

Table of Contents

1	Introduction	3

1.1 Problem statement	3

1.2 Goal	3

1.3 Non-goal	3

1.4 Terminology	3

2	Technical note Solution	4

2.1 Definitions	4

2.2 Technical note behavior	4

2.2.1 Use scenario	4

2.2.2 Modeling outline	5

2.2.3 ebXML Specifications Taxonomy tModel	6

2.2.4 Common ebXML tModels	6

2.2.5 Registering ebXML services	10

2.2.6 Searching ebXML services and components	12

2.2.7 Scenario variation: Using a CPA template	14

3	References	15

3.1 Normative	15

Appendix A. Acknowledgments	16

Appendix B. Revision History	17

Appendix C. Notices	18

# Introduction

This note describes the way to model ebXML-based services and ebXML components such as Collaboration Protocol Profile and Business Process Specification Schema. It provides a practical guidance on how to use a UDDI registry as the registry for ebXML. It will help people to adopt UDDI as their registry, and prompt use of it in real business scene.

## Problem statement

Some standard bodies initiated a trial which uses ebXML framework for business to business transactions, and some companies started to use ebXML technologies for their businesses. While the use of Web service technologies in real business field is greatly expanding, UDDI is adopted as an important infrastructure technology which realizes a metadata registry for Web services. Under the circumstances, it is no wonder that a company who provides ebXML-based services wants to register his services to a UDDI registry.  When a company and its trading partner initiate business transactions using ebXML, each have to obtain the other’s profile to configure their ebXML runtime systems.  It is likely that they want to use a UDDI registry to look up each other’s ebXML Collaboration Protocol Profile.

A recommended way of modeling services and components which are conformant to ebXML specifications is needed.

## Goal

This note provides the way:

To model an ebXML-based service.

To register an ebXML-based service and ebXML components to a UDDI registry.

To inquire of a UDDI registry an ebXML-based service and ebXML components.

## Non-goal

This note does not intend to show the way:

To merge UDDI and ebXML Registry & Repository.

To substitute ebXML Registry & Repository with UDDI registry.

To transit from ebXML Registry & Repository to UDDI registry (and vice versa).

## Terminology

The key words must, must not, required, shall, shall not, should, should not, recommended, may, and optional in this document are to be interpreted as described in [RFC2119].

# Technical note Solution

## Definitions

ebXML

ebXML is a common XML-based e-business framework which consists of some distinct technologies.

ebXML Message Services

ebXML Messaging Services are communication protocol for e-business. It extends the SOAP protocol to add features required for business-to-business transaction such as security, authentication, reliability. [ebMS1][ebMS2]

ebXML Collaboration Protocol Profile and Agreement (CPPA)

This is a specification which defines CPP and CPA. [ebCPPA1][ebCPPA2]

ebXML Collaboration Protocol Profile (CPP)

CPP describes a service provider’s information such as the business processes, document formats, and some communication parameters required to communicate with a trading partner.  Each trading partner creates its CPP in advance. Before starting to do business with a partner via ebXML communication, trading partners exchange their CPPs each other, recognize the other’s technical capability, negotiate for common ground, and build CPA (Collaboration Protocol Agreement).

ebXML Collaboration Protocol Agreement (CPA)

Information which is agreed between trading partners that enables them to communicate each other is expressed as a CPA.  A CPA can be formed from two (or more) CPPs, or may be created from a template for CPA.

ebXML CPA template

CPA template is a trading partner’s “fill in the blanks” proposal to a prospective trading partner.  It has placeholding values that are replaced by the actual values. Sometimes a CPA template is used to form a CPA, instead of merging two CPPs.

ebXML Business Process Specification Schema (BPSS)

BPSS provides machine readable description of business processes. [ebBPSS]

## Technical note behavior

### Use scenario

We should assume a typical use scenario to clarify issues and requirements. The items below are assumptions to make it simple and practical:

A fictitious standard body, named “ABC Consortium” has created a standardized business process for a particular industry, and describes them as ebXML BPSS.

A fictitious company A (seller) and B (buyer) have created their own CPP.

Company A has provided an ebXML-based service Sa which is conformant to the standard process defined by the body.

Then, we assume some steps below which realize “UDDI as the registry for ebXML components”:

- ABC Consortium creates a tModel of the standard business process and publishes it.

- Company A registers the location of its CPP as a business service.

- Company A registers a service Sa

- Company B finds A’s service Sa using a UDDI registry.

- Company B locates A’s CPP using a UDDI registry.

The figure 1 shows these five steps.

Figure 1:  Use scenario:  “UDDI as the registry for ebXML components”

After accomplishing these five steps, Company B obtains A’s CPP. Then it can begin to negotiate and build CPA, and can start business with Company A, while these phases have no relation to a UDDI registry.

The following sections provide a recommended way of modeling which covers this scenario.

### Modeling outline

### In this technical note, three types of tModels below are defined:

### Specifications Taxonomy tModel:

### This taxonomy is used to categorize each specification. It is useful to categorize the common ebXML tModels (see below), and it helps their discovery.

### Common ebXML tModels:

### These tModels refer specific version of ebXML specifications/concepts, such as CPP v1.0, BPSS v1.01, Message Service v2.0, and so on.  It is desirable that these tModels should be prepared in the UDDI Business Registry so that anybody can refer them.

### Proprietary tModels:

### These tModels refer specific instances or implementations of ebXML specifications. For instance, a certain business process described in ebXML BPSS is an instance of BPSS, and it can be defined as a proprietary tModel.

### Services and components owned by a specific party are modeled as business services respectively.

### The way described in this technical note applies to both UDDI v2 and v3 registry, though illustrated examples are written in v2.

### ebXML Specifications Taxonomy tModel

ebXML is a framework and consists of distinct technical specifications. In UDDI, tModels are often categorized using information which helps their discovery. Before defining tModels related to ebXML specification, we define an ebXML Specifications Taxonomy tModel which is used to categorize common tModels described in the following section..

ebXML Specification Taxonomy tModel:

tModel Name:		ebxml-org:specifications

tModel Description:		ebXML Specifications Taxonomy

tModel UDDI Key (V3):	uddi:ubr.uddi.org:categorization:ebxml.org:specifications

Evolved V1, V2 format Key:	uuid:xxxxxxxx-xxxx-xxxx-xxxx-xxxxxxxxxx01 (to be derived)

Categorization:		categorization

Checked:			No

<tModel tModelKey=”uuid:xxxxxxxx-xxxx-xxxx-xxxx-xxxxxxxxxx01”>

<name>ebxml-org:specifications</name>

<description xml:lang=”en”>ebXML Specifications Taxonomy</description>

<overviewDoc>

<overviewURL>http://www.ebxml.org/specs/</overviewURL>

</overviewDoc>

<categoryBag>

<keyedReference

tModelKey=”uuid:C1ACF26D-9672-4404-9D70-39B756E62AB4”

keyName=”uddi-org:types”

keyValue=”categorization” />

<keyedReference

tModelKey=”uuid:C1ACF26D-9672-4404-9D70-39B756E62AB4”

keyName=”uddi-org:types”

keyValue=”unchecked” />

</categoryBag>

The following values are defined for this ebXML Specifications taxonomy. These values are useful for classifying ebXML related tModels and are helpful for others who want to find those tModels.

ebXML:CPPA	ebXML Collaboration Protocol Profile and Agreement

ebXML:MS	ebXML Message Service

ebXML:BPSS	ebXML Business Process Specification Schema

Please note that this tModel does not represent ebXML specifications themselves, but a categorization system.

### Common ebXML tModels

In UDDI, a service interface is associated with tModels which refer to the technical specification of the interface in its overviewDoc. Those tModels represent service type information. In the case of ebXML specifications, Message Service, CPP, CPA template and BPSS are appropriate for tModels to represent service type information.

Here, we define these tModels as common tModels. “Common” means that the tModels are created and published in advance, and referred by all users who use a UDDI as the registry for ebXML services and components.  The tModels as follows:

ebXML Message Service v1.0 tModel:

tModel Name:		ebxml-org:MessageService:v1_0

tModel Description:		ebXML Message Service v1.0

tModel UDDI Key (V3):	uddi:ubr.uddi.org:protocol:ebxml.org:MessageService:v1.0

Evolved V1, V2 format Key:	uuid:xxxxxxxx-xxxx-xxxx-xxxx-xxxxxxxxxx02 (to be derived)

Categorization:		protocol

<tModel tModelKey=”uuid:xxxxxxxx-xxxx-xxxx-xxxx-xxxxxxxxxx02”>

<name>ebxml-org:MessageService:v1_0</name>

<description xml:lang=”en”>ebXML Message Service v1.0</description>

<overviewDoc>

<overviewURL>http://www.ebxml.org/specs/ebMS.pdf</overviewURL>

</overviewDoc>

<categoryBag>

<keyedReference

tModelKey=”uuid:C1ACF26D-9672-4404-9D70-39B756E62AB4”

keyName=”uddi-org:types”

keyValue=”protocol” />

<keyedReference

tModelKey=” uuid:xxxxxxxx-xxxx-xxxx-xxxx-xxxxxxxxxx01”

keyName=”ebxml-org:specifications”

keyValue=”ebXML:MS” />            <!—- Message Service spec. -->

</categoryBag>

ebXML Message Service v2.0 tModel:

tModel Name:		ebxml-org:MessageService:v2_0

tModel Description:		ebXML Message Service v2.0

tModel UDDI Key (V3):	uddi:ubr.uddi.org:protocol:ebxml.org:MessageService:v2.0

Evolved V1, V2 format Key:	uuid:xxxxxxxx-xxxx-xxxx-xxxx-xxxxxxxxxx03 (to be derived)

Categorization:		protocol

<tModel tModelKey=”uuid:xxxxxxxx-xxxx-xxxx-xxxx-xxxxxxxxxx03”>

<name>ebxml-org:MessageService:v2_0</name>

<description xml:lang=”en”>ebXML Message Service v2.0</description>

<overviewDoc>

<overviewURL>http://www.ebxml.org/specs/ebMS2.pdf</overviewURL>

</overviewDoc>

<categoryBag>

<keyedReference

tModelKey=”uuid:C1ACF26D-9672-4404-9D70-39B756E62AB4”

keyName=”uddi-org:types”

keyValue=”protocol” />

<keyedReference

tModelKey=” uuid:xxxxxxxx-xxxx-xxxx-xxxx-xxxxxxxxxx01”

keyName=”ebxml-org:specifications”

keyValue=”ebXML:MS” />            <!—- Message Service spec. -->

</categoryBag>

ebXML CPP v1.0 tModel:

tModel Name:		ebxml-org:CollaborationProtocolProfile:v1_0

tModel Description:		ebXML Collaboration Protocol Profile v1.0

tModel UDDI Key (V3):	uddi:ubr.uddi.org:protocol:ebxml.org:CollaborationProtocolProfile:v1.0

Evolved V1, V2 format Key:	uuid:xxxxxxxx-xxxx-xxxx-xxxx-xxxxxxxxxx04 (to be derived)

Categorization:		protocol

<tModel tModelKey=”uuid:xxxxxxxx-xxxx-xxxx-xxxx-xxxxxxxxxx04”>

<name>ebxml-org:CollaborationProtocolProfile:v1_0</name>

<description xml:lang=”en”>ebXML Collaboration Protocol Profile v1.0 </description>

<overviewDoc>

<overviewURL>http://www.ebxml.org/specs/ebCPP.pdf</overviewURL>

</overviewDoc>

<categoryBag>

<keyedReference

tModelKey=”uuid:C1ACF26D-9672-4404-9D70-39B756E62AB4”

keyName=”uddi-org:types”

keyValue=”protocol” />

<keyedReference

tModelKey=” uuid:xxxxxxxx-xxxx-xxxx-xxxx-xxxxxxxxxx01”

keyName=”ebxml-org:specifications”

keyValue=”ebXML:CPPA” />      <!—- This belongs to CPPA spec. -->

</categoryBag>

ebXML CPP v2.0 tModel:

tModel Name:		ebxml-org:CollaborationProtocolProfile:v2_0

tModel Description:		ebXML Collaboration Protocol Profile v2.0

tModel UDDI Key (V3):	uddi:ubr.uddi.org:protocol:ebxml.org:CollaborationProtocolProfile:v2.0

Evolved V1, V2 format Key:	uuid:xxxxxxxx-xxxx-xxxx-xxxx-xxxxxxxxxx05 (to be derived)

Categorization:		protocol

<tModel tModelKey=”uuid:xxxxxxxx-xxxx-xxxx-xxxx-xxxxxxxxxx05”>

<name>ebxml-org:CollaborationProtocolProfile:v2_0</name>

<description xml:lang=”en”>ebXML Collaboration Protocol Profile v2.0 </description>

<overviewDoc>

<overviewURL>http://www.ebxml.org/specs/ebcpp-2.0.pdf</overviewURL>

</overviewDoc>

<categoryBag>

<keyedReference

tModelKey=”uuid:C1ACF26D-9672-4404-9D70-39B756E62AB4”

keyName=”uddi-org:types”

keyValue=”protocol” />

<keyedReference

tModelKey=” uuid:xxxxxxxx-xxxx-xxxx-xxxx-xxxxxxxxxx01”

keyName=”ebxml-org:specifications”

keyValue=”ebXML:CPPA” />     <!—- This belongs to CPPA spec. -->

</categoryBag>

ebXML CPA v1.0 Template tModel:

tModel Name:		ebxml-org:CollaborationProtocolAgreement:v1_0:Template

tModel Description:		ebXML Collaboration Protocol Agreement v1.0 Template

tModel UDDI Key (V3):	uddi:ubr.uddi.org:protocol:ebxml.org:CollaborationProtocolAgreement:v1.0:Template

Evolved V1, V2 format Key:	uuid:xxxxxxxx-xxxx-xxxx-xxxx-xxxxxxxxxx06 (to be derived)

Categorization:		protocol

<tModel tModelKey=”uuid:xxxxxxxx-xxxx-xxxx-xxxx-xxxxxxxxxx06”>

<name>ebxml-org:CollaborationProtocolAgreement:v1_0:Template</name>

<description xml:lang=”en”>

ebXML Collaboration Protocol Agreement v1.0 Template

</description>

<overviewDoc>

<overviewURL>http://www.ebxml.org/specs/ebCPP.pdf</overviewURL>

</overviewDoc>

<categoryBag>

<keyedReference

tModelKey=”uuid:C1ACF26D-9672-4404-9D70-39B756E62AB4”

keyName=”uddi-org:types”

keyValue=”protocol” />

<keyedReference

tModelKey=” uuid:xxxxxxxx-xxxx-xxxx-xxxx-xxxxxxxxxx01”

keyName=”ebxml-org:specifications”

keyValue=”ebXML:CPPA” />      <!—- This belongs to CPPA spec. -->

</categoryBag>

ebXML CPA v2.0 Template tModel:

tModel Name:		ebxml-org:CollaborationProtocolAgreement:v2_0:Template

tModel Description:		ebXML Collaboration Protocol Agreement v2.0 Template

tModel UDDI Key (V3):	uddi:ubr.uddi.org:protocol:ebxml.org:CollaborationProtocolAgreement:v2.0:Template

Evolved V1, V2 format Key:	uuid:xxxxxxxx-xxxx-xxxx-xxxx-xxxxxxxxxx07 (to be derived)

Categorization:		protocol

<tModel tModelKey=”uuid:xxxxxxxx-xxxx-xxxx-xxxx-xxxxxxxxxx07”>

<name>ebxml-org:CollaborationProtocolAgreement:v2_0:Template</name>

<description xml:lang=”en”>

ebXML Collaboration Protocol Agreement v2.0 Template

</description>

<overviewDoc>

<overviewURL>http://www.ebxml.org/specs/ebcpp-2.0.pdf</overviewURL>

</overviewDoc>

<categoryBag>

<keyedReference

tModelKey=”uuid:C1ACF26D-9672-4404-9D70-39B756E62AB4”

keyName=”uddi-org:types”

keyValue=”protocol” />

<keyedReference

tModelKey=” uuid:xxxxxxxx-xxxx-xxxx-xxxx-xxxxxxxxxx01”

keyName=”ebxml-org:specifications”

keyValue=”ebXML:CPPA” />     <!—- This belongs to CPPA spec. -->

</categoryBag>

ebXML Business Process Specification Schema v1.01 tModel:

tModel Name:		ebxml-org:BusinessProcessSpecificationSchema:v1_01

tModel Description:		ebXML Business Process Specification Schema v1.01

tModel UDDI Key (V3):	uddi:ubr.uddi.org:protocol:ebxml.org:BusinessProcessSpecificationSchema:v1.01

Evolved V1, V2 format Key:	uuid:xxxxxxxx-xxxx-xxxx-xxxx-xxxxxxxxxx08 (to be derived)

Categorization:		protocol

<tModel tModelKey=”uuid:xxxxxxxx-xxxx-xxxx-xxxx-xxxxxxxxxx08”>

<name>ebxml-org:BusinessProcessSpecificationSchema:v1_01</name>

<description xml:lang=”en”>ebXML Business Process Specification Schema v1.01 </description>

<overviewDoc>

<overviewURL>http://www.ebxml.org/specs/ebBPSS.pdf</overviewURL>

</overviewDoc>

<categoryBag>

<keyedReference

tModelKey=”uuid:C1ACF26D-9672-4404-9D70-39B756E62AB4”

keyName=”uddi-org:types”

keyValue=”protocol” />

<keyedReference

tModelKey=” uuid:xxxxxxxx-xxxx-xxxx-xxxx-xxxxxxxxxx01”

keyName=”ebxml-org:specifications”

keyValue=”ebXML:BPSS” />      <!—- This belongs to BPSS spec. -->

</categoryBag>

Since these tModels are categorized by ebXML Specifications Taxonomy (ebxml-org:specifications) defined in the previous section, they are easy to find.

### Registering ebXML services

Above tModels defined so far enable us to model and register ebXML-based services in a UDDI registry. In accordance with the scenario presented at the section 2.2.1, we show the details of steps one by one.

#### A standard body registers proprietary tModel of BPSS instance

In this section, the step below is shown:

- ABC Consortium creates a tModel of the standard business process and publishes it.

It is natural to regard a business process definition as one of technical characteristics of a service interface, since it describes business choreography which the service behaves. Every registered businessService which is conformant to an ebXML BPSS description should be associated with a tModel of the description.

In our scenario, a fictitious standard body, ABC Consortium defines a standard business process (here, we call it as “ABC Standard Srocess #1”) which is widely used by the consortium members. The consortium describes it as a BPSS instance.

Assuming that the instance is located at “http://abc.org/process_1.bpss”, we define the tModel like below:

tModel Name:		abc-org:StandardProcess:1

tModel Description:		ABC Consortium’s standard process #1

tModel UDDI Key:		uuid:xxxxxxxx-xxxx-xxxx-xxxx-xxxxxxxxxbp1

Categorization:		specification

<tModel>

<name>abc-org:StandardProcess:1</name>

<description xml:lang=”en”> ABC’s standard process #1</description>

<overviewDoc>

<overviewURL>http://abc.org/process_1.bpss</overviewURL>

</overviewDoc>

<categoryBag>

<keyedReference

tModelKey=”uuid:C1ACF26D-9672-4404-9D70-39B756E62AB4”

keyName=”uddi-org:types”

keyValue=”specification” />

<keyedReference

tModelKey=”uuid:xxxxxxxx-xxxx-xxxx-xxxx-xxxxxxxxxx08”

keyValue=” ebxml-org:BusinessProcessSpecificationSchema:v1_01” />

</categoryBag>

</tModel>

ABC Consortium registers this tModel using save_tModel. Later, it is referred from a service whose choreography is conformant to this BPSS instance.

#### Company A registers CPP

In this section, the step below is shown:

- Company A registers the location of its CPP as a business service.

In UDDI, all business services must be associated with a business entity. A company must first create a businessEntity if it decides to register a service which is conformant to ebXML. This note recommends that a location of CPP should be registered as an accessPoint in a businessService. Assuming that Company A’s CPP is located at “http://a.com/a.cpp”, its businessEntity and businessService as follows:

<businessEntity>

<name xml:lang=”en”>Company A</name>

<contacts>…</contacts>

<businessServices>

<businessService>

<name xml:lang=”en”>Company A’s CPP</name>

<description xml:lang=”en”>Company A’s CPP</description>

<bindingTemplates>

<bindingTemplate>

<accessPoint URLType=”http”>

http://a.com/a.cpp

</accessPoint>

<description xml:lang=”en”> A’s CPP is here!</description>

<tModelInstanceDetails>

<tModelInstanceInfo

tModelKey=”uuid:xxxxxxxx-xxxx-xxxx-xxxx-xxxxxxxxxx04”>

<description>

ebxml-org:CollaborationProtocolProfile:v1_0

</description>

</tModelInstanceInfo>

</tModelInstanceDetails>

</bindingTemplate>

</bindingTemplates>

</businessService>

</businessServices>

</businessEntity>

The business service above can be regarded as a service which delivers A’s CPP. Company A issues save_business API with above contents to register its CPP.

#### Company A registers an ebXML-based service

In this section, the step below is shown:

- Company A registers a service Sa.

Now Company A has a businessEntity which contains one businessService that delivers CPP. Then it can add a service Sa which utilizes ebXML Message Services protocol and is conformant to the standard process #1 defined by ABC Consortium, as a new businessService. Assuming that Sa is an online wine shop and is provided at “http://a.com/wine/acceptPurchaseOrder”, the new businessService as follows:

<businessService>

<name xml:lang=”en”>A’s online wine shop</name>

<description xml:lang=”en”>an ebXML-based service</description>

<bindingTemplates>

<bindingTemplate>

<accessPoint URLType=”http”>

http://a.com/wine/acceptPurchaseOrder

</accessPoint>

<description xml:lang=”en”>A’s ebXML-based service</description>

<tModelInstanceDetails>

<tModelInstanceInfo

tModelKey=”uuid:xxxxxxxx-xxxx-xxxx-xxxx-xxxxxxxxxx02”>

<description>ebxml-org:MessageService:v1_0</description>

</tModelInstanceInfo>

<tModelInstanceInfo

tModelKey=”uuid:xxxxxxxx-xxxx-xxxx-xxxx-xxxxxxxxxbp1”>

<description>abc-org:StandardProcess:1</description>

</tModelInstanceInfo>

</tModelInstanceDetails>

</bindingTemplate>

</bindingTemplates>

<categoryBag>

<keyedReference

tModelKey=”uuid:CD153257-086A-4237-B336-6BDCBDCC6634”

keyValue=”50.20.22.05”

keyName=”UNSPSC:Sparkling_Wine” /> <!—- Service category info -->

</categoryBag>

</businessService>

Company A issues save_service API with above contents to register the service.

### Searching ebXML services and components

In this section, we show the way that Company B (buyer) finds a seller and retrieves a seller’s CPP.  Since the examples below are for explanation, they may sometimes be redundant a little.

#### Company B finds a service

In this section, the step below is shown:

- Company B finds A’s service Sa using a UDDI registry.

UDDI provides some sort of search capabilities. It is possible to find by business name, service category, service type, and so on. In our scenario, it is assumed that Company B (buyer) is capable of doing business using ebXML framework, adopts the ABC Consortium’s standard business process #1, and wants to consume a service which is provided by an ebXML-ready seller.

The example below finds a service provider who has its own ebXML CPP (which means that it is ebXML-ready):

<find_business>

<tModelBag>

<!-- ebxml-org:CollaborationProtocolProfile:v1_0 -->

<tModelKey>uuid:xxxxxxxx-xxxx-xxxx-xxxx-xxxxxxxxxx04</tModelKey>

</tModelBag>

</find_business>

Company B issues an above inquiry and gets a businessList like below as a result:

<businessList>

<businessInfos>

<businessInfo businessKey=”...Company A’s businessKey...”>

<name>Company A</name>

<serviceInfos>

<serviceInfo serviceKey=”...serviceKey of CPP...”>

<name>Company A’s CPP</name>    <!-- Company A has a CPP! -->

</serviceInfo>

<serviceInfo serviceKey=”...serviceKey of an ebXML service...”>

<name>A’s online wine shop</name>

</serviceInfo>

</serviceInfos>

</businessInfo>

</businessInfos>

</businessList>

Now Company B finds that Company A is a seller who provides en ebXML-based online service. Then, Company B checks if Company A provides a service that is conformant to the ABC Consortium’s standard business process, which Company B also adopts.

The example below finds Company A’s service which utilizes ebXML Message Services as communication protocol and which is conformant to the standard process #1 defined by the ABC Consortium.

<find_service businessKey=”...Company A’s businessKey...”>

<tModelBag>

<!-- ebxml-org:MessageService:v1_0 -->

<tModelKey>uuid:xxxxxxxx-xxxx-xxxx-xxxx-xxxxxxxxxx02</tModelKey>

<!-- abc-org:StandardProcess:1 -->

<tModelKey>uuid:xxxxxxxx-xxxx-xxxx-xxxx-xxxxxxxxxbp1</tModelKey>

</tModelBag>

</find_service>

Now Company B finds the Company A’s ebXML service which meets the requirements, then the next step is to exchange each other’s CPP to negotiate communication parameters.

#### Company B obtains A’s CPP

In this section, the step below is shown:

- Company B locates A’s CPP using a UDDI registry.

The example below finds Company A’s business service which contains the location information of A’s CPP.

<find_service businessKey=”...Company A’s businessKey...”>

<tModelBag>

<!-- ebxml-org:CollaborationProtocolProfile:v1_0 -->

<tModelKey>uuid:xxxxxxxx-xxxx-xxxx-xxxx-xxxxxxxxxx04</tModelKey>

</tModelBag>

</find_service>

Company B issues an above inquiry and gets a serviceList like below as a result:

<serviceList>

<serviceInfos>

<serviceInfo businessKey=”...Company A’s businessKey...”

serviceKey=”...serviceKey of CPP...”>

<name>Company A’s CPP</name>

</serviceInfo>

</serviceInfos>

</serviceList>

Now Company B got a serviceKey of business service which contains information of A’s CPP, then Company B issues get_serviceDetail API to retrieve an access point information of the CPP.

<get_serviceDetail>

<serviceKey>”...serviceKey of CPP...”</serviceKey>

</get_serviceDetail>

Company B gets full information of the businessService and knows that Company A’s CPP is located at “http://a.com/a.cpp”.

Finally Company A and B can exchange each other’s CPP, start to negotiate to build CPA, and consume Sa .

In a real system, multiple inquiries shown in the examples above will not be used since they are redundant and inefficient. But this section still helpful to understand concepts.

Scenario variation: Using a CPA template

While [ebCPPA2] suggests that a CPA is formed from two CPPs, it also mentions an alternative way which uses a CPA template to create a CPA. Since a CPA template represents one company’s proposed configuration of service interface to perform business collaboration, the other trading partner only have to replace the placeholder values to form an agreed CPA.  It is known as an easier way of CPA negotiation process.

In our scenario described in section 2.2.1, a CPA template provided Company A (seller) can be used as an alternative to Company A’s CPP. In this case, Company A can publish a business service shown below at the Step 2:

<businessService>

<name xml:lang=”en”>Company A’s CPA Template</name>

<description xml:lang=”en”>

CPA template provided by Company A

</description>

<bindingTemplates>

<bindingTemplate>

<accessPoint URLType=”http”>

http://a.com/a.cpa-template

</accessPoint>

<description xml:lang=”en”>CPA template is here!</description>

<tModelInstanceDetails>

<tModelInstanceInfo

tModelKey=”uuid:xxxxxxxx-xxxx-xxxx-xxxx-xxxxxxxxxx06”>

<description>

ebxml-org:CollaborationProtocolAgreement:v1_0:Template

</description>

</tModelInstanceInfo>

</tModelInstanceDetails>

</bindingTemplate>

</bindingTemplates>

</businessService>

# References

## Normative

[RFC2119]	S. Bradner, Key words for use in RFCs to Indicate Requirement Levels, http://www.ietf.org/rfc/rfc2119.txt, IETF RFC 2119, March 1997.

[UDDIV3]	L. Clément et al, UDDI V3.0 Published Specification, http://uddi.org/pubs/uddi-v3.00-published-20020719.pdf, OASIS UDDI Spec TC Committee Specification, July 2002.

[ebBPSS]	Business Process Project Team, ebXML Business Process Specification Schema Version 1.01, http://www.ebxml.org/specs/ebBPSS.pdf, May 2001.

[ebCPPA1]	ebXML Trading-Partners Team, Collaboration-Protocol Profile and Agreement Specification Version 1.0, http://www.ebxml.org/specs/ebCPP.pdf, May 2001.

[ebCPPA2]	OASIS ebXML Collaboration Protocol Profile and Agreement Technical Committee, Collaboration-Protocol Profile and Agreement Specification Version 2.0, http://www.ebxml.org/specs/ebcpp-2.0.pdf, September 2002.

[ebMS1]	ebXML Transport, Routing & Packaging Team, Message Service Specification Version 1.0, http://www.ebxml.org/specs/ebMS.pdf, May 2001.

[ebMS2]	OASIS ebXML Messaging Services Technical Committee, Message Service Specification Version 2.0, http://www.ebxml.org/specs/ebMS2.pdf, April 2002.

Acknowledgments

The author(s) would like to thank Joel Munter, Sean MacRoibeaird, and Ed Mooney for their initial contribution of this theme.

Revision History

| Rev | Date | By Whom | What |
| --- | --- | --- | --- |
| 1 | January 8, 2003 | Keisuke Kibakura | Initial version. |
| 2 | January 31, 2003 | Keisuke Kibakura | Clarification statement added: - Support for UDDI v2 and v3. - No intent to substitute ebXML RR. Improved modeling: - Restructured spec taxonomy - Addition of common tModels Brief outline of modeling Terminology clarification - CPPA, CPP, CPA, CPA template Added scenario variation. |

Notices

OASIS takes no position regarding the validity or scope of any intellectual property or other rights that might be claimed to pertain to the implementation or use of the technology described in this document or the extent to which any license under such rights might or might not be available; neither does it represent that it has made any effort to identify any such rights. Information on OASIS's procedures with respect to rights in OASIS specifications can be found at the OASIS website. Copies of claims of rights made available for publication and any assurances of licenses to be made available, or the result of an attempt made to obtain a general license or permission for the use of such proprietary rights by implementors or users of this specification, can be obtained from the OASIS Executive Director.

OASIS invites any interested party to bring to its attention any copyrights, patents or patent applications, or other proprietary rights which may cover technology that may be required to implement this specification. Please address the information to the OASIS Executive Director.

Copyright  © OASIS Open 2002. All Rights Reserved.

This document and translations of it may be copied and furnished to others, and derivative works that comment on or otherwise explain it or assist in its implementation may be prepared, copied, published and distributed, in whole or in part, without restriction of any kind, provided that the above copyright notice and this paragraph are included on all such copies and derivative works. However, this document itself does not be modified in any way, such as by removing the copyright notice or references to OASIS, except as needed for the purpose of developing OASIS specifications, in which case the procedures for copyrights defined in the OASIS Intellectual Property Rights document must be followed, or as required to translate it into languages other than English.

The limited permissions granted above are perpetual and will not be revoked by OASIS or its successors or assigns.

This document and the information contained herein is provided on an “AS IS” basis and OASIS DISCLAIMS ALL WARRANTIES, EXPRESS OR IMPLIED, INCLUDING BUT NOT LIMITED TO ANY WARRANTY THAT THE USE OF THE INFORMATION HEREIN WILL NOT INFRINGE ANY RIGHTS OR ANY IMPLIED WARRANTIES OF MERCHANTABILITY OR FITNESS FOR A PARTICULAR PURPOSE.

# Footnotes

This tModel is not used in the scenario, but is used in its variation. See Section 2.2.7.

In the examples in this technical note, v2 format key is used. Note that entity key compatibility with v3 and earlier versions of UDDI should be considered unless the standard body intends to use this proprietary tModel in a closed environment only (e.g. a private registry). See Section 10 “Multi-Version Support” in [UDDIV3].

The ways to exchange CPP and to negotiate CPA are not defined here.

# Comments

Substitute with a calculated one.