## Slide 1: Development Process and Testing Tools for Content Standards OASIS Symposium: The Meaning of Interoperability May 9, 2006
Simon Frechette, NIST

## Slide 2: Outline
Process For Developing Content Standards: The Model Development Life Cycle (MDLC)
Overview of NIST XML-Related Testing Tools
Notes: The purpose of this slide is to tell the audience what we want to tell them and to hint that the proposed MDLC, the IDEF model is not an absolute model. However, it serves our purpose to motivate our research work around MDLC to help the industry achieve interoperability.

## Slide 3: Who We Are
US Department of Commerce (DOC)
National Institute of Standards and Technology (NIST)
Manufacturing Engineering Laboratory (MEL)
Manufacturing Systems Integration Division (MSID)

## Slide 4
Manufacturing B2B
Integration
Manufacturing
Metrology Interoperability
(Inspection)
Process
Plant
Construction
Information
Integration
Integrated
Circuit Design and
Manufacturing
Component
Validation
Semantic Web R&D
“Generic” Testing Infrastructure and Tool Development (e.g., XML, ebXML, schema quality, test case generation)
Legacy Migration
Through
Semantic
Mapping
Automotive
Inventory
Visibility
CAD/CAM
Integration
Simulation
System
Integration
NIST Interoperability Testbed

## Slide 5: Some Specific Problems in Model (Specification) Development
Unbounded specification growth
Semantically duplicate/overlapping terms, components, and documents are created
Limited reuse
Classic interoperability problems are revisited over and over again
Large-scale harmonization is hard to achieve
And… process takes too long and costs too much
Notes: - This slide talks about problems associated with the evolution.

## Slide 6: Content Standards are Bridges
Design the bridge
Test the design
Build the foundation
Assemble the structure
Test the bridge
Many components are standardized
Many standards are used
Building Process:

## Slide 7: Model Development Life Cycle
A guideline for building industrial strength data exchange bridges, that provides:
Detailed analysis of the development process for content standards
Architecture for implementing that process
Outline of requirements for tools
Roadmap to the standards landscape

## Slide 8: Model Development Life Cycle
Notes: - The Data Exchange Requirements input includes all the detailed information requirements for integration. This information can be captured in a number of different models: use case models, integration activity models, object/information models, and process models.
- The Library of Semantically Coherent XML Schemas output is a collection of data interchange terms and data structures
represented as XML Schemas [XSD]. Terms and data structures should contain unique semantics or overlapping semantics, but no duplicate semantics. Overlapping can come about by extension, restriction, redefinition, or subsumption. Where direct relationships cannot be established or duplication cannot be eliminated, the models should be formally annotated. The library may incorporate XML-based content standards and will include new XML content models. The resulting library should also contain supporting data to help maximize the reusability of its terms and data structures.
Supporting data include but are not limited to, classification schemes for categorization, the models provided in the
information exchange requirements, sample XML instance reference data, meta-data, more expressive semantic models,
and documentation.
-The Change Requests output reflects the cyclical nature of a typical life cycle. For example, a request is made to the
owning entity to modify their model in order to fully cover requirements or maintain consistency. This results in a
change to the existing library.
- XML Schema Specification controls the syntactical and grammatical representation of terms and data structures for the
data exchange specification. It also limits the expressiveness with which the relationships between overlapping data
structures can be modeled.
-XML Schema Design Guidelines force compliance of the resulting XML Schemas to a selected set of design principles.
These design principles may be preferred ways of utilizing the XML Schema specification when alternatives exist,
common data structure patterns, or required meta-data. While some of the guidelines appear to be mere stylistic options, their consistent use is critical to supporting schema reuse.
-Supporting material is the collection of source material for understanding the systems, data, and specifications involved
in the integration. It may include implementation documentation, business rules, classification schemes, and external
domain ontologies that help clarify the intent of the data and specifications.
Although Existing Data may be viewed as part of the data exchange requirements input, the purpose here is as reference information to support requirement satisfaction and compatibility analyses.
- XML Tools encompass tools that implement the XML Schema specification and related XML standards. These include
XML schema validators; XML parsers and validators, and editors; and, other tools that implement utility standards
related to XML such as the XML Path language [XPATH] and the Extensible Stylesheet Transformation Language
[XSLT].
Rule-based Engines are mechanisms used to test conformance of schemas to design guidelines and other requirements. Schematron [Jelliffe 2003] is a specific example of a rule-based engine that is used with XML standards including the XML Schema. A traditional rule-based expert system such as the Java-based Expert System Shell [Friedman-Hill 2002] may be used as well.
- Semantic Analysis Tools enhance reuse of the semantic model or XML Schemas. They may support discovery, harmonization,

## Slide 9: Decomposition of the MDLC
Existing Schemas & Classification Scheme
A2
Model Validation
A3
Model Piloting
A4
Model
Registration
A1
Model Discovery
A5
Model Integration
Specification
Tools
Rule
Based
Engines
Specification
Design
Rules
Specification
Reference
Data
Implementation
Data
Business
Rules
Implementation
Context
Guidelines
Schematron
XSLT
Engine
Annotation
Tools
Test Suites
Implementation
Documentation
External
Ontologies
Classification
Assistant
Semantic
Similarity
Measure
Semantic
Alignment
Algorithm
External
Ontologies
Registry &
Repository
Qualified
Schemas
Data
Exchange
Requirements
Business
Forms
Change
Requests
Link
Annotations
Change Requests
Table
Of
Terms
Existing Schemas
Registry Entry
Classification
Scheme
New
Specifications
Semantic Aware
Lookup Assistant
Requirement Gaps
Discovered Schema
Spread
sheet
Annotation
Tools
Schema
Semantics
Existing
Data
Testing occurs at each step in the process
Notes: Model Discovery Typically, integration projects first try to identify relevant, existing XML Schemas. This process is called Model Discovery. The first activity should always be to discover any model that fits the scope of the project as captured in the data exchange requirements.
- Model Validation: The Model Validation activity takes as input an initial information specification, such as the XML schema, produced by the Model Discovery activity. Since an XML schema is not like other pieces of software - it has no execution requirements. Includes tests for requirements coverage and design quality. Model Validation (A2) can take much iteration of its sub-activities, but the end result is a valid schema meeting a given set of quality criteria along with documentation describing the schema and how it is to be used. That documentation contains reference data and the table of terms representing the naming conventions.
- Model Piloting: To solve a real integration problem, we must exchange information between specific software applications, which may impose additional requirements on the XML schemas. So, while the schemas in our repository presumably cover most of these additional requirements, certain modifications may be necessary. For one XML Schema this may involve additional usage criteria specific to the applications to be integrated. For another, it may also involve a simplification to make it directly applicable to the applications to be integrated. The Model Piloting activity deals with these issues by making the available schemas usable for the specific integration problem at hand.
The Model Registration activity organizes the schemas and related materials within a registry and stores them in a repository that is accessible to other activities (see Figure 7). Other supplemental information such as schema version, hierarchical namespace, dependencies, associative semantics, and context information may be stored as well. This supports a multi-dimensional and structured search of the registry; hence, discovery of the schemas is more efficient.
- The Model Integration activity ensures that new schemas and extensions are semantically coherent and, where possible, eliminates duplicate and overlapping schemas.

## Slide 10: Types of Testing
Validation Testing – the assessment of the underlying specification to which products will be developed. Validation testing attempts to evaluate the completeness, correctness, and consistency of a data model to be used for a standard.
Conformance Testing – the assessment of a whether a product meets the requirements of a particular specification or standard.
Interoperability Testing – the assessment of a product to determine if it will exchange and share information (interoperate) with another product.
Performance Testing – the assessment of the performance characteristics of a product such as throughput and response time under various conditions.
Robustness Testing – the assessment of a product to determine how well it performs when supplied data which is difficult to processes, such as, extremely large data sets or data which contain errors.

## Slide 11: Overview of some NIST XML-Related Testing Tools
XML Schema Validation Tool
XML Instance Validation Tool
Quality of Design Tool
Content Validation and Testing System
XML Schema Naming Assister
Schematron Editor Tool
Classification Assistant (Research)
Semantic-Aware Lookup Assistant (Research)
Semantic Alignment Tool (Research)

## Slide 12: XML Schema Validation Tool
Objective: Ensure that schemas are compatible with a selected set of parsers
Core Functionality: Validate one or more schemas or schema extensions with multiple selected parsers and schema files stored in a repository
Status: Prototype available at http://www.nist.gov/msid/validation

## Slide 14: XML Instance Validation Tool
Objective: Ensure that schemas are compatible with a selected set of parsers, a set of sample data, a previous set of sample data (when the schemas have gone through changes)
Core Functionality: Automatically validate one or more instance files against associated schemas with multiple selected parsers (in batch mode)
Status: Prototype is available at http://www.nist.gov/msid/validation

## Slide 15: Quality of Design (QOD) Tool
Objective: Ensure that XML schemas conform to a selected set of design practices - use of common and valid terms, NDR conformance, use of the XML Schema structures that enhance reusability, maintainability, clarity, and interoperability
Core Functionality: A flexible environment for specifying and executing best practice rules against the schemas
Status: Beta – Available upon request. Contact Serm Kulvatunyou: serm@nist.gov
Notes: - Give examples of best practices

## Slide 17: Content Validation and Testing System (CVTS)
Objective: Capture, codify, and execute business rules that are not captured in the XML Schema.
Core Functionality: Store, publish, and execute business rules for checking instance data for conformance with those rules.
Status: on-line at http://syseng.nist.gov/b2bTestbed/projects/semanticChecking

## Slide 18: XML Schema Naming Assister
Objective: Ensure that type, element, and attribute names used in schemas are consistent within the schema and conform to ISO 11179 Naming Convention
Core Functionality: Decompose names into Object Class, Property, and Representation Term tokens, validate them using a table of terms, and suggest alternate names
Status: Prototype. Available at http://www.nist.gov/msid/Naming_Assister.html
Notes: - Give examples of best practices

## Slide 19: Schematron Editor Tool
Objective: Assist a user in creating Schematron Rules
Core Functionality: Create Schematron with little or no knowledge of XPATH/XSLT syntax through expression wizards that allow drag-n-drop elements from an imported XML schema business document
Status: Prototype – available on Sourceforge site http://www.sf.net/projects/cs-wizard

## Slide 20: Summary
MDLC is a recipe for building robust data exchange specifications
We are using it to drive development of tools and testing capabilities
  Validation Service
  Quality of Design tool
Maximizes reuse of tools to serve a diverse collection of customers
Notes: We have identified five high-level activities involved in creating and maintaining XML schemas used for systems integration.
We also described a number of existing tools developed at NIST and elsewhere to support the execution of
these activities. Finally, we outlined several semantic-based tools that have been conceptualized but not yet implemented.
We believe that these activities and tools are key to achieving coherence in the life cycle of a schema. Without these
tools, the registry is nothing but a simple file store. Our future work will mainly focus on making the semantic tools
a reality while continuing to generalize and improve the existing tools.

## Slide 21: Mother’s Day...
is this Sunday